FORD 6.0L AMSOIL DUAL FILTER MOUNT OIL LINE ROUTING

It has come to our attention that all 6.0L diesel motors equipped with the AMS Oil dual filtration system have been installed incorrectly.  The “in” and “out” ports have been plumbed incorrectly causing a reverse flow through the oil filters.

Please refer to the attached photos and diagram for the correct routing of these lines from the adaptor block to the filter mount.  The lines should be crossed between these two locations. You can check if they are crossed by tracing the lines from the adaptor block to the filter mount.  You will need to check the entire length of the lines as they may be crossed anywhere, even above the fuel filter.

If they are not crossed, you will need to disconnect the connections at either the filter mount or the adaptor block (the adaptor block may be easier to access) and reverse the two hoses.  When doing this, the filters should also be changed as you will be reversing the flow of the filtration.  An ideal time to swap the lines would be the next time the filters are due for a change.

As with any issue that comes up, Sportsmobile has been very diligent in researching the affects of this incorrect installation.  We were very pleased to find that there have been no adverse affects to the motor or oil system due to this incorrect installation.  Vans with different mileage and different model years have been tested to ensure that all angles are covered.  The oil analysis for these vehicles has confirmed that the oil is within the normal boundaries of the manufacturers specifications.  Furthermore, testing has also been completed to ensure that the motor has been operating under normal oil pressure.  These tests also concluded that the motor has been operating under normal conditions as specified by the manufacturer.

If you have any questions, need additional assistance, or want to speak with a Sportsmobile tech, please call and ask for Heber or Peter.